## Slide 1
Decoding Continuous Motion Trajectories of Upper Limb from EEG Signals
Based on Feature Selection and Nonlinear Methods
Group Members 1.Uplaksh Bishnoi(2024EE11162) 2.Piyush Joshi(2024EE10373) 3.Dravya Kunal Mehta(2024EE11099) 4.Abhishek Anand(2024EE30209) 5.Mehak Singh(2024EE30531)

## Slide 2
BCI systems restore motor independence through precise 3D hand trajectory reconstruction
OBJECTIVE
Reconstruct continuous 3D hand trajectories from non-invasive EEG signals to restore independence for patients with severe paralysis.
SIGNIFICANCE
Translating neural activity into motion is critical for enabling patients to regain control through assistive robotic devices, bridging the gap between intent and action.
CORE CHALLENGE
Overcoming the low signal-to-noise ratio inherent in scalp EEG and the complex, non-linear mapping between brain signals and physical kinematics.

## Slide 3
The TFP framework optimizes decoding through temporal fixation, spatial selection, and nonlinear regression
Time-window Fixation
Precise selection of task-related EEG segments (400 samples) to maximize information density and reduce ambient noise.
Spatial Feature Selection
PCA-based dimensionality reduction extracts the most relevant neural components from 31 EEG channels, isolating core patterns.
Nonlinear Regression
3rd-order polynomial mapping captures complex, non-linear movement dynamics that linear models often fail to represent.

## Slide 4
Decoding Pipeline logic
Pre Processing
0.1–40 Hz Butterworth Band-pass
FastICA for EOG/EMG rejection
Resampling to 256 Hz
Global normalization (-1 to 1)
PCA on 31-channel input
Threshold: 90% Variance
3rd Order Poly expansion
Ridge Regression (α=10)
Prevents matrix overfitting
Trial-wise coefficient logging
Average Top 50% coefficients
Noise-resistant trajectory
Feature Selection
Nonlinear Model
TFP Stability

## Slide 5
A robust preprocessing pipeline ensures high data integrity and effective signal cleaning
Signal Cleaning
4th-order Butterworth band-pass (0.1–40 Hz) and ICA remove EOG/EMG artifacts.
Standardization
EEG is standardized; kinematics normalized to [-1, 1] for consistent scaling.
Temporal Alignment
Resampled to 256 Hz with a focused 1.56s window per trial to align features.
Data Integrity
Missing values handled by linear interpolation and run-wise quality checks.

## Slide 6
PCA-driven dimensionality reduction preserves 90% of variance while optimizing computation
SPATIAL FILTERING
PCA on 31 channels isolates key neural components and removes redundancy.
SELECTION CRITERION
90%
Components selected to capture 90% cumulative variance.
COMPUTATIONAL EFFICIENCY
74.76%
PCA reduces computation time substantially while retaining accuracy.
FEATURE PRESERVATION
Preserves spatial features crucial for upper-limb decoding.

## Slide 7
3rd-order polynomial regression captures the non-linear complexity of human motion
MODEL ARCHITECTURE
y(x) = a₀ + Σ bᵢxᵢ + Σ cᵢⱼxᵢxⱼ + Σ dᵢⱼₖxᵢxⱼxₖ + ε
Non-linear Mapping: Models complex relationships between neural activity and 3D coordinates.
Higher-order Features: Captures interaction terms between neural components for improved decoding.
TRAINING & REGULARIZATION
Ridge Regression: Uses L2 regularization (alpha=10) for stability in high-dimensional spaces.
Class-Specific Optimization: Separate models are optimized for 6 movement classes and 3 spatial dimensions.
TFP Basis: Provides a robust foundation for translating neural features into motion trajectories.

## Slide 8
Automated 5-fold cross-validation ensures model stability and generalizability
ROBUST VALIDATION
Implementation of 5-fold Cross-Validation provides a reliable and unbiased estimate of decoding performance across 15 subjects, ensuring results are not dependent on specific data partitions.
AUTOMATED PIPELINE
An end-to-end processing script handles subject-wise analysis, seamlessly integrating preprocessing, PCA, and regression stages for consistent and reproducible results.
MODEL STABILITY
Training coefficients are averaged using the top 50% largest values (TFP method) to create representative, noise-resistant models that capture core movement patterns.
GENERALIZABILITY
This structured approach ensures that the decoding models are robust against trial-to-trial noise and generalizable to unseen motor execution data.

## Slide 9
The TFP method achieves superior quantitative performance with an average PCC of 0.42
PERFORMANCE COMPARISON (PCC)
Method
X-Axis
Y-Axis
Z-Axis
Mean
MLR (Linear)
0.153
0.143
0.146
0.147
Ridge (RR)
0.118
0.113
0.116
0.115
TFP (Proposed)
0.36
0.5
0.4
0.42
Significant Improvement
TFP demonstrates a 236% to 253% improvement in correlation over traditional linear methods.
Balanced Decoding
Consistent performance across all three spatial dimensions (X, Y, Z) confirms robust 3D reconstruction.
Our 14th and 15th run results
0.774
0.919
0.788
0.859
0.975
0.916

## Slide 10
Strategic Conclusions
Key Insights
Technical Efficiency
Future Vision
Nonlinear polynomial mapping effectively bridges the gap between low-delta EEG and complex kinematics, outperforming linear MLR by ~250%.
PCA feature selection isolates critical neural components, reducing redundancy by 74% while maintaining 90% of signal variance.
Scaling to real-time robotic limb control and exploring LSTM architectures to model the temporal dependencies of human motion.
Thank You!